## Slide 1: Trust Management in Wireless Sensor Networks
Peter Chapin
Christian Skalka
April 3, 2013

## Slide 2: What Problem are we Solving?
Internet
Base Station
Base Station

## Slide 3: Sensor Network RPC
Wireless networks…
  Volatile
  Unreliable
  Have limited power (nodes must sleep)
Synchronous RPC not suitable
  Invoker can’t afford to wait for a reply
    (that might never come)
SpartanRPC is asynchronous

## Slide 4: Tasks vs Duties
nesC supports tasks… asynchronous execution
Tasks have limitations
  Can’t take parameters
  Must be defined in the same module that posts
SpartanRPC extends nesC tasks to duties
  Can take parameters
  Can be posted remotely

## Slide 5: Duty Example
interface LEDControl { duty void setLEDs(uint8_t mask); }
module ClientC { uses interface LEDControl; } implementation { … post LEDControl.setLEDs(42);
… }
module ServerC { provides remote interface LEDControl; } implementation { duty void LEDControl.setLEDs (uint8_t mask) {
…
}
}

## Slide 6: nesC Wiring
Component wiring is static
  Program can not change connections at run time
SpartanRPC models inter-node connections as dynamic wires
configuration AppC { }
implementation {
components MainC, LEDControllerC;
MainC.LEDControl -> LEDControllerC;
…
}

## Slide 7: Dynamic Wires
RemoteSelectorC provides the ComponentManager interface
A component_set is an array of remote component IDs
configuration AppC { }
implementation {
components ClientC, RemoteSelectorC;
ClientC.LEDControl -> [RemoteSelectorC].LEDControl;
}
interface ComponentManager {
command component_set elements( );
}

## Slide 8: RT0 Trust Management
A.r ← E
A.r ← B.s
A.r ← B.s.t
A.r ← B.s ∩ C.t
WSN.sensor ← UVM.student
WSN.sensor ← WSN.admin
WSN.admin ← UVM.depts.staff
UVM.depts ← CS
CS.staff ← CS.faculty
CS.faculty ← Jill
Server Policy
Client Certificates
Design of a Role Based Trust Management Framework, Li et. al.

## Slide 9: RT0 Authorization
Each RT0 credential is a Datalog predicate
WSN.admin ← UVM.depts.staff
mem(wsn, admin, X) :- mem(uvm, depts, Y), mem(Y, staff, X).
mem(cs, faculty, jill)
mem(cs, staff, jill)
mem(uvm, depts, cs)
mem(wsn, admin, jill)
mem(wsn, sensor, jill)
Semantics is minimum
model implied by
credentials

## Slide 10: Security Example 1
interface LEDControl { duty void setLEDs(uint8_t mask); }
module ClientC { uses interface LEDControl; } implementation { … post LEDControl.setLEDs(42);
… }
module ServerC { provides remote interface LEDControl
requires “UVM.admin”; } implementation { duty void LEDControl.setLEDs (uint8_t mask) {
…
}
}

## Slide 11: Security Example 2
configuration AppC { }
implementation {
components ClientC, RemoteSelectorC;
enable “*” for ClientC.LEDControl ->
[RemoteSelectorC].LEDControl;
}

## Slide 12: Architecture: Credential Exchange
Certificate
Sender
Certificate
Storage
(ROM)
Certificate
Receiver
Key Storage
Credential
Storage
(+ Model)
Client
Server

## Slide 13: Architecture: Message Exchange
Generated
Stub
Session Key Cache
Generated
Skeleton
Session Key Cache
Credential
Storage
(+ Model)
Client
Server

## Slide 14: Memory Requirements
Item | Size (bytes) | N | Total (bytes) | Location
Certificates | 166 (max) | Variable | Variable | ROM
Public Keys | 40 | 12 | 480 | RAM
Credentials | 16 | 12 | 192 | RAM
Model Tuples | 6 | 16 | 96 | RAM
Session Keys | 22 | 10 | 220 | RAM
Runtime System | ~25 KiB | 1 | ~25 KiB | ROM
Packet buffers currently 46 bytes; certificates are sent in fragments

## Slide 15: Processing Time
Parameter | Rate
Baseline Messages | 128 messages/s
RPC (no security) | 119 messages/s
RPC (with MAC computation) | 87 messages/s
Certificate Verification | ~90 seconds each
D-H Key Exchange | ~60 seconds each
Model Update | 370 μs
Mote Hardware: MSP430F1611 (10 KiB RAM, 48 KiB ROM, 8 MHz)
Operating system: TinyOS v2.1.2

## Slide 16: Conclusions
Trust management in WSNs is feasible
Most security processing done in background
  Only (hardware assisted) MAC computation on messages.
  High initial latency; minimal runtime overhead.
ECC cryptography is feasible
Memory overhead significant, but manageable

## Slide 17: Future Work
Enhance implementation
Demonstrate on full-scale application (Snow Cloud?)
Get paper accepted!
https://github.com/pchapin/sprocket